## Slide 1
Vision is all you need
Ananye Agarwal, Ashish Kumar
References
Agarwal, A. et al. (2022) Legged locomotion in challenging terrains using egocentric vision, arXiv.org. Available at: https://arxiv.org/abs/2211.07638 (Accessed: December 1, 2022).
Figure 1: We train our locomotion policy in two phases to avoid rendering depth for too many samples. In phase 1, we use RL to train a policy π 1 that has access to scandots that are cheap to compute. In phase 2, we use π 1 to provide ground truth actions which another policy π 2 is trained to imitate.
Two-Step Training Phase in a simulation (Fig 1)
Reinforcement Learning of a policy with a light-weight variant of depth images
Supervised Learning on whole Depth Image to fine-tune the learned policy
2. Methods
Transferability of obtained policy in simulation to real-world without any fine-tuning
Possibility of traversing various environments with high success (Fig 2)
3. Results
In certain instances this approach does not work well because of a mismatch between simulation and real world
Future work on leveraging data collected in the real world to yield better performances
4. Conclusion
Figure 2: We show success rates and time-to-failure (TTF) for our method and the blind baseline on curbs, stairs, stepping stones and gaps.
Ananye Agarwal Carnegie Mellon
ananye@agarwal.com
@ananye_agarwal
Scan the QR-Code for more information and videos of the dog in action
Traditional approaches have decomposed the problem of locomotion into mapping and foothold tracking
This work presents the first end-to-end locomotion system capable of traversing different environments
1. Introduction
Ashish Kumar Berkley
ashish_@kumar.com
@ashish_kumar
End-To-End locomotion shows the potential for robots to
traverse challenging terrains